## Slide 1: Application Acceleration with High-Level Synthesis
110062703 梁浩祥
LabB no.9 Sparse Matrix Multiplication

## Slide 2: Overall system
Sparse matrix unlike usual matrix is mostly contains 0
Storing in standard data structure will have a lot of waste.
Hence, we use compressed row storage(CRS) for storing

## Slide 3: Implementation

## Slide 4: Implementation

## Slide 5: Analyze

## Slide 6: Optimization
Directives
  Unroll
  Pipeline
  Cyclic
  block

## Slide 7: Optimization
case | L1 | L2 | time | Iteration latency | Interval | Trip count | DSP | DD | LUT
Baseline | x | x | 7.256 | 13 | 5 | 4 | 5 | 1165 | 1388
1 | x | pipeline | 7.256 | 13 | 5 | 4 | 5 | 1165 | 1388
2 | pipeline | x | 7.256 | 12 | 5 | 4 | 5 | 1165 | 1345
3 | Unroll 2 | x | 7.256 | 13 | 5 | 2 | 5 | 1466 | 1799
4 | x | pipeline Unroll 2 | 7.256 | 18 | 10 | 4 | 5 | 1466 | 1655
5 | x | pipeline Unroll 2 Cyclic 2 | 7.256 | 18 | 10 | 4 | 5 | 1660 | 1874
6 | x | pipeline Unroll 4 | 7.256 | 28 | 20 | 4 | 5 | 1677 | 2120
7 | X | pipeline Unroll 4 Cyclic 4 | 7.247 | 27 | 20 | 4 | 5 | 2285 | 2728
8 | X | pipeline Unroll 8 | 7.256 | 48 | 40 | 4 | 5 | 2065 | 2988
9 | X | pipeline Unroll 8 Cyclic 8 | 7.561 | 47 | 40 | 4 | 5 | 3399 | 4724
10 | x | pipeline Unroll 8 block 8 | 7.274 | 47 | 40 | 4 | 5 | 3969 | 4293

## Slide 8: Observered and Learned
Set pipline II = 2 or 1 will cause violation, but don’t set anything won’t
Xilinx HLS is very easy to use compare with RTL
  No worry for change of functionality after pipeline, unroll, data partition.
  Compile time is negligible
  Agile design space exploration
  Many directives options.
And more open public information compare with Stratus HLS
  A lot of documentation online
  A lot of discussions/ tutorial online